## Slide 1
❤️ CardioRisk AI
A Multimodal Deep Learning System for Smartphone-Based Cardiovascular Risk Assessment
Hussain Mahabub
2111015642
Course: CSE 499A – Capstone Project | Supervisor: Shahnewaz Department of Computer Science & Engineering North South University

## Slide 2
CSE 499A CAPSTONE | WHAT?
The Global Crisis & Project Scope
The Cardiovascular Crisis
• Cardiovascular diseases (CVDs) cause 17.9M global deaths annually (32% of all deaths).
• Early risk detection is hindered by heavy clinical dependency and high equipment costs.
• Traditional checkups require ECG machines, phlebotomy labs, and specialist interpretation.
• Severely inaccessible in developing nations and rural medical deserts.
What We Are Doing (CardioRisk AI)
• Developing a smartphone-based multimodal cardiovascular risk assessment platform.
• Integrating 6 distinct physiological & clinical modalities.
• Deploying deep convolutional networks (CNNs) & calibrated Gradient Boosting.
• Providing live Explainable AI (SHAP) and counterfactual lifestyle paths.
• Establishing an API-first foundation ready for dedicated IoT hardware in 499B.

## Slide 3
CSE 499A CAPSTONE | WHY?
Literature Review & Identified Research Gaps
Existing Solutions
• Clinical Calculators: Framingham & ASCVD rely only on static tabular data (10-yr horizon).
• Attia et al. (2019): Deep CNN on 12-lead ECG (AUC 0.870).
• Poplin et al. (2018): Deep CNN on Retinal Fundus (AUC 0.754).
• Potes et al. (2016): CNN+RNN on Heart Sounds (Acc 86.2%).
Identified Gaps
• Gap 1: Single Modality Limits. Missing cross-domain signal correlation.
• Gap 2: Black-Box AI. Lack of interpretability blocks clinical adoption.
• Gap 3: Deployment Deficit. Research models rarely translated into usable mobile software.
Our Justification
• Multimodal fusion significantly outperforms isolated single-modality checks.
• SHAP values + Counterfactual recommendations build clinical trust.
• FastAPI + Streamlit full-stack architecture ensures portable accessibility.

## Slide 4
CSE 499A CAPSTONE | HOW?
System Architecture & Engineering Design
Layered Architecture (CSE 327)
• Presentation Layer: Interactive Streamlit Web App (Port 8501) with live risk gauge & What-If simulator.
• Middleware Layer: Async FastAPI backend (Port 8000) with REST endpoints & DSP pipelines.
• Model Layer: 1D-CNN (ECG), 2D-CNN (Heart Sound), Calibrated Gradient Boosting (Tabular).
• Data Access Layer: SQLite relational persistence with planned RDS PostgreSQL migration.
Six Integrated Modalities
• 1. Clinical Tabular: Age, Systolic/Diastolic BP, BMI, Lipids.
• 2. Electrocardiogram (ECG): 12-lead QRS, QT, ST elevation.
• 3. Heart Sounds (PCG): Phonocardiogram SNR & spectral centroid.
• 4. PPG / HRV: Camera video frame photoplethysmography.
• 5. SCG: Seismocardiography via phone accelerometer.
• 6. Retinal Imaging: Microvascular tortuosity & density.

## Slide 5
CSE 499A CAPSTONE | HOW?
Deep Learning Models & Signal Processing (DSP)
Model Architectures
• ECG 1D-CNN: 4 Conv1D Blocks + BatchNorm + MaxPool + GlobalAveragePool + Dense (Dropout 0.5/0.3).
• Heart Sound 2D-CNN: Mel-spectrogram input processing with 2D convolutions & spatial pooling.
• Tabular Classifier: Gradient Boosting with Platt Scaling / Isotonic Calibration for true probabilities.
Laptop DSP Preprocessing Pipeline
• PPG Processing: Spatial green-channel extraction, cubic spline interpolation (30 Hz), Butterworth bandpass (0.7-4.0 Hz).
• Heart Sound DSP: Downsampling (44.1 kHz -> 2 kHz), spectral subtraction for fan noise removal, bandpass filter (20-400 Hz).
• Signal Matching: Standardizes laptop webcam/mic signals to match clinical training datasets (PTB-XL & CinC 2016).

## Slide 6
CSE 499A CAPSTONE | HOW?
Dynamic Confidence-Weighted Ensemble Fusion
The Static Weighting Paradox
• Initial static weighting (0.40 ECG / 0.40 HS / 0.20 Tabular) caused accuracy dilution (dropped from 86.0% to 81.5%).
• A static ensemble forces the system to trust uncertain, noisy modalities.
• Fixed weights fail when sensor noise degrades a single modality channel.
Confidence-Weighted Solution
• Confidence is dynamically computed: Confidence = 2 * |P - 0.5|.
• Weights adaptively sum to 1 across all available modalities.
• Confident models take priority; ambiguous models (P ~ 0.5) receive near-zero weight.
• Result: Ensemble accuracy boosted to 82.50% (+1.00% over static).

## Slide 7
CSE 499A CAPSTONE | RESULTS
Preliminary Implementation Results (499A)
Model / Pipeline | Dataset / Source | Samples | Accuracy | AUC-ROC
ECG 1D-CNN (Calibrated) | PTB-XL Dataset | 21,837 | 86.00% | 0.935
Heart Sound CNN (Calibrated) | PhysioNet CinC 2016 | 3,126 | 80.50% | 0.898
Tabular Gradient Boosting | Kaggle CVD Dataset | 70,000 | 77.00% | 0.908
Static Ensemble (Baseline) | Synthetic Paired Test | - | 81.50% | 0.920
Dynamic Ensemble (Ours) | Synthetic Paired Test | - | 82.50% | 0.923
Key Takeaway
• Synthetic Validation: Independent test validation proves dynamic multimodal fusion provides high system resilience.
• Fault Tolerance: If hardware noise corrupts ECG in real-time, the system automatically shifts weight to acoustic & clinical channels.

## Slide 8
CSE 499A CAPSTONE | HOW?
Explainable AI (XAI) & Clinical Features
Explainability (SHAP & Counterfactuals)
• SHAP TreeExplainer: Computes local mathematical contributions for each clinical factor in real-time (e.g., BP: +0.15, Age: +0.12).
• Counterfactual Explanations: Algorithmically discovers minimal lifestyle changes required to drop a patient into low-risk categories.
• Eliminates the medical 'black box' problem to build doctor-patient trust.
Interactive Clinical Tools
• What-If Simulator: Real-time UI widgets allow clinicians to simulate blood pressure, smoking, and activity modifications.
• Bulk Patient Processing: Batch CSV import to evaluate and classify large patient rosters in seconds.
• Doctor Dashboard: Aggregated risk distribution graphs and persistent patient assessment logs via SQLite.

## Slide 9
CSE 499A CAPSTONE | NEXT STEPS
Future Work & Hardware Integration (CSE 499B)
Physical IoT Hardware Stack (~$95 BOM)
• Microcontroller: ESP32 (Wi-Fi / BLE dual-core processing).
• ECG Sensor: AD8232 integrated analog front-end.
• PPG Sensor: MAX30102 pulse oximetry sensor.
• Heart Sounds: MAX9814 electret microphone amplifier.
• Kinematics / SCG: ADXL345 3-axis accelerometer for chest micro-vibrations & motion artifact cancellation.
Software & Validation Roadmap
• Firmware: FreeRTOS task scheduling with hardware timer interrupts for microsecond-accurate time-series synchronization.
• Stacking Meta-Learner: Train a secondary model to learn non-linear cross-modality correlations, closing the remaining baseline gap.
• Cloud Migration: AWS EC2 backend hosting + AWS RDS PostgreSQL for high concurrency.
• Clinical User Testing: End-to-end evaluation on real test participants.

## Slide 10
CSE 499A CAPSTONE | REFERENCES
References (IEEE Format)
• [1] World Health Organization, 'Cardiovascular diseases (CVDs),' WHO Fact Sheet, 2021.
• [2] E. J. Benjamin et al., 'Heart Disease and Stroke Statistics—2023 Update,' Circulation, vol. 147, no. 8, pp. e93-e621, 2023.
• [3] S. F. Weng et al., 'Can machine-learning improve cardiovascular risk prediction using routine clinical data?,' PLOS ONE, 2017.
• [4] Z. I. Attia et al., 'An artificial intelligence-enabled ECG algorithm for identification of atrial fibrillation,' The Lancet, 2019.
• [5] P. Wagner et al., 'PTB-XL, a large publicly available electrocardiography dataset,' Scientific Data, vol. 7, p. 154, 2020.
• [6] C. Liu et al., 'An open access database for the evaluation of heart sound algorithms,' Physiological Measurement, 2016.
• [7] S. M. Lundberg and S.-I. Lee, 'A unified approach to interpreting model predictions,' in NeurIPS, 2017, pp. 4765-4774.

## Slide 11
Thank You!
CardioRisk AI: Smartphone-Based Cardiovascular Risk Assessment CSE 499A Capstone Defense
Questions & Feedback