## Slide 1
CardioRisk AI
A Multimodal Deep Learning System for Smartphone-Based Cardiovascular Risk Assessment
Presenter: Hussain Mahabub (Student ID: 2111015642) | Section 10 – Group 10
Course: CSE 499A – Senior Design Capstone Project | Supervisor: Shahnewaz Siddique
Department of Computer Science & Engineering, North South University

## Slide 2
CSE 499A CAPSTONE | WHAT?
The Global Crisis & Project Scope
The Cardiovascular Crisis
• Cardiovascular diseases (CVDs) cause 17.9M global deaths annually (32% of all deaths).
• Early risk detection is hindered by heavy clinical dependency and high equipment costs.
• Traditional checkups require ECG machines, phlebotomy labs, and specialist interpretation.
• Severely inaccessible in developing nations and rural medical deserts.
What We Are Doing (CardioRisk AI)
• Developing a smartphone-based multimodal cardiovascular risk assessment platform.
• Integrating 6 distinct physiological & clinical modalities into a unified system.
• Deploying deep convolutional networks (CNNs) & calibrated Gradient Boosting.
• Providing live Explainable AI (SHAP) and counterfactual lifestyle pathways.
• Establishing an API-first foundation ready for dedicated IoT hardware in 499B.

## Slide 3
CSE 499A CAPSTONE | WHY?
Literature Review & Identified Research Gaps
Existing Solutions & Benchmarks
• Clinical Calculators: Framingham & ASCVD rely only on static tabular data (10-yr horizon).
• Attia et al. (2019): Deep 1D-CNN on 12-lead ECG (AUC 0.870).
• Potes et al. (2016): CNN + RNN on Heart Sounds / PCG (Acc 86.2%).
• Poplin et al. (2018): Deep CNN on Retinal Fundus (AUC 0.754).
Identified Gaps & Our Justification
• Gap 1: Single Modality Limits. Missing cross-domain physiological correlation.
• Gap 2: Black-Box AI. Lack of interpretability blocks clinical adoption.
• Gap 3: Deployment Deficit. Research models rarely translated into mobile software.
• Our Justification: Multimodal fusion + SHAP values + Counterfactuals build clinical trust.
• FastAPI + Streamlit full-stack architecture ensures portable, real-time accessibility.

## Slide 4
CSE 499A CAPSTONE | HOW?
System Architecture & Engineering Design
Layered Architecture (CSE 327)
• Presentation Layer: Interactive Streamlit Web App (Port 8501) with live risk gauge & What-If simulator.
• Middleware Layer: Async FastAPI backend (Port 8000) with REST endpoints & DSP pipelines.
• Model Layer: 1D-CNN (ECG), 2D-CNN (Heart Sound), Calibrated Gradient Boosting (Tabular).
• Data Access Layer: SQLite relational persistence with planned RDS PostgreSQL migration.
Six Integrated Modalities
• 1. Clinical Tabular: Age, Systolic/Diastolic BP, BMI, Lipids, Glycemia.
• 2. Electrocardiogram (ECG): 12-lead QRS, QT interval, ST elevation.
• 3. Heart Sounds (PCG): Phonocardiogram SNR & spectral centroid.
• 4. PPG / HRV: Camera video frame photoplethysmography (HRV metrics).
• 5. SCG: Seismocardiography via phone accelerometer vibrations.
• 6. Retinal Imaging: Microvascular tortuosity & vessel density.

## Slide 5
CSE 499A CAPSTONE | HOW?
Deep Learning Models & Signal Processing (DSP)
Model Architectures
• ECG 1D-CNN: 4 Conv1D Blocks + BatchNorm + MaxPool + GlobalAveragePool + Dense (Dropout 0.5/0.3).
• Heart Sound 2D-CNN: Mel-spectrogram input processing with 2D convolutions & spatial pooling.
• Tabular Classifier: Gradient Boosting with Platt Scaling / Isotonic Calibration for true probabilities.
Digital Signal Processing (DSP) Pipeline
• PPG Processing: Spatial green-channel extraction, cubic spline interpolation (30 Hz), Butterworth bandpass (0.7-4.0 Hz).
• Heart Sound DSP: Downsampling (44.1 kHz -> 2 kHz), spectral subtraction for fan noise removal, bandpass filter (20-400 Hz).
• Signal Matching: Standardizes consumer webcam/mic signals to match clinical training datasets (PTB-XL & CinC 2016).

## Slide 6
CSE 499A CAPSTONE | HOW?
Dynamic Confidence-Weighted Ensemble Fusion
Static vs. Dynamic Fusion
• Static Weighting (40% ECG / 40% HS / 20% Tabular) achieves 94.65% on clean data.
• Vulnerability: Static ensembles force the system to trust degraded, noisy modalities.
• Fixed weights fail when sensor noise corrupts a single hardware channel.
Confidence-Weighted Solution & Fault Tolerance
• Confidence is dynamically computed: Confidence = 2 * |P - 0.50|.
• Weights adaptively sum to 1 across active modalities.
• Decisive models take priority; ambiguous models (P ~ 0.50) receive near-zero weight.
• Dynamic ensemble achieves 93.65% accuracy with superior fault tolerance.
• Automated weight reduction: Noise drops corrupted channel weight by 38.12%.

## Slide 7
CSE 499A CAPSTONE | RESULTS
Preliminary Implementation Results (499A)
Model / Pipeline | Dataset / Source | Samples | Accuracy | AUC-ROC
ECG 1D-CNN | PTB-XL | 2,000 | 93.05% | 0.9838
Heart Sound 2D-CNN | PhysioNet CinC 2016 | 3,126 | 75.85% | 0.8540
Tabular (Gradient Boosting) | Kaggle CVD | 69,971 | 68.95% | 0.7643
Static Ensemble (40/40/20) | Combined (Clean) | — | 94.65% | 0.9879
Dynamic Ensemble (Proposed) | Confidence-Weighted | — | 93.65% | 0.9832
Key Takeaway: Clean Accuracy vs. Fault Tolerance
• Static Fusion is optimal for clean signals (94.65% Acc, 0.9879 AUC).
• Dynamic Fusion trades minor clean-signal margin for critical fault tolerance (93.65% Acc)[cite: 8, 11].
• Under noise injection, dynamic weighting automatically drops corrupted sensor weight from 41.25% down to 3.13% (maintaining 81.55% accuracy).

## Slide 8
CSE 499A CAPSTONE | HOW?
Explainable AI (XAI) & Clinical Features
Explainability (SHAP & Counterfactuals)
• SHAP TreeExplainer: Computes local mathematical contributions for each factor (e.g., BP: +0.12, Age: +0.15)[cite: 7, 11].
• Counterfactual Engine: Discovers minimal lifestyle changes required to drop patient risk to normal thresholds (e.g., -8.5% for smoking cessation)[cite: 7, 11].
• Eliminates the medical 'black box' problem to build doctor-patient trust.
Interactive Clinical Tools
• What-If Simulator: Real-time UI widgets allow clinicians to simulate blood pressure and lifestyle modifications.
• Bulk Patient Processing: Batch CSV import to evaluate and classify large patient rosters in seconds.
• Doctor Dashboard: Aggregated risk distribution graphs and persistent patient assessment logs via SQLite.

## Slide 9
CSE 499A CAPSTONE | NEXT STEPS
Future Work & Hardware Integration (CSE 499B)
Physical IoT Hardware Stack (~$95 BOM)
• Microcontroller: ESP32 (Wi-Fi / BLE dual-core processing) ($15).
• ECG Sensor: AD8232 integrated analog front-end ($20).
• PPG Sensor: MAX30102 pulse oximetry sensor ($15).
• Heart Sounds: MAX9814 electret microphone amplifier ($10).
• Kinematics / SCG: ADXL345 3-axis accelerometer for chest micro-vibrations ($10).
Software & Validation Roadmap
• Firmware: FreeRTOS task scheduling with hardware timer interrupts for microsecond-accurate time-series synchronization.
• Stacking Meta-Learner: Train a secondary model to learn non-linear cross-modality correlations.
• Cloud Migration: AWS EC2 backend hosting + AWS RDS PostgreSQL for high concurrency.
• Clinical User Testing: End-to-end evaluation on real test participants.

## Slide 10
CSE 499A CAPSTONE | REFERENCES
References (IEEE Format)
Cited Literature
• [1] World Health Organization, 'Cardiovascular diseases (CVDs),' WHO Fact Sheet, 2021.
• [2] E. J. Benjamin et al., 'Heart Disease and Stroke Statistics—2023 Update,' Circulation, vol. 147, no. 8, pp. e93-e621, 2023[cite: 1, 11].
• [3] S. F. Weng et al., 'Can machine-learning improve cardiovascular risk prediction using routine clinical data?,' PLOS ONE, 2017[cite: 1, 11].
• [4] Z. I. Attia et al., 'An artificial intelligence-enabled ECG algorithm for identification of atrial fibrillation,' The Lancet, 2019[cite: 1, 11].
• [5] P. Wagner et al., 'PTB-XL, a large publicly available electrocardiography dataset,' Scientific Data, vol. 7, p. 154, 2020[cite: 1, 11].
• [6] C. Liu et al., 'An open access database for the evaluation of heart sound algorithms,' Physiological Measurement, 2016[cite: 1, 11].
• [7] S. M. Lundberg and S.-I. Lee, 'A unified approach to interpreting model predictions,' in NeurIPS, 2017, pp. 4765-4774[cite: 1, 11].

## Slide 11
Thank You!
CardioRisk AI: Smartphone-Based Cardiovascular Risk Assessment
CSE 499A Capstone Defense | Questions & Feedback